## Slide 1: Computer Networks
BMTA Training, June 30, 2019

## Slide 2: Agenda
Computer Network Reviews
Network Protocols
  Hands-On #1: Simple Network Tools
Ethernet
  Hands-On #2: Ethernet Switch
Network Protocols
  Hands-On #3: OSPF Routing Protocol
Application Protocols
  Hands-On #4: DHCP

## Slide 3: Computer Network Reviews

## Slide 4: Connected Devices

## Slide 5: Resources in a Network
Client-Server
Peer-to-Peer

## Slide 6: Topologies
Physical Topology
Logical Topology

## Slide 7: Components in Networks
Devices

## Slide 8: Components in Networks
Media

## Slide 9: Components in Networks
Services

## Slide 10: Types of Networks
Local Area Networks (LAN)

## Slide 11: Types of Networks
Wide Area Networks (WAN)

## Slide 12: Types of Networks
The Internet

## Slide 13: Supporting Network Architecture
Four basic characteristics that the underlying architectures need to address in order to meet user expectation:
  Fault Tolerance
  Scalability
  Quality of Service (QoS)
  Security

## Slide 14: Fault Tolerance

## Slide 15: Scalability

## Slide 16: Quality of Service (QoS)
Examples of priority decisions for an organization might include:
Time-sensitive communication – increase priority for services like telephony or video distribution.
Non time-sensitive communication – decrease priority for web page retrieval or email.
High importance to organization – increase priority for production control or business transaction data.
Undesirable communication – decrease priority or block unwanted activity, like peer-to-peer file sharing or live entertainment.

## Slide 17: Security

## Slide 18: Network Protocols

## Slide 19: Network Model

## Slide 20: Protocol Suites

## Slide 21: TCP/IP Protocol Suite

## Slide 22: IEEE Standards

## Slide 23: Protocol Data Units (PDUs)

## Slide 24: Network Addresses and Data Link Addresses
Same Network

## Slide 25: Network Addresses and Data Link Addresses
Remote Network

## Slide 26: Hands-On #1: Simple Network Tools

## Slide 27: Ethernet

## Slide 28: Ethernet
One of the most widely used LAN technologies
Operates in the data link layer and the physical layer
Family of networking technologies that are defined in the IEEE 802.2 and 802.3 standards
Supports data bandwidths of 10, 100, 1000, 10,000, 40,000, and 100,000 Mbps (100 Gbps)
Two separate sub layers of the data link layer to operate –Logical link control (LLC) and the MAC sublayers

## Slide 29: Ethernet: LLC
Handles communication between upper and lower layers (Network Layer vs. MAC Sublayer).
Takes the network protocol data and adds control information to help deliver the packet to the destination.

## Slide 30: Ethernet: MAC
Provides three primary functions:
  Frame delimiting –Identifies a group of bits that make up a frame, synchronization between the transmitting and receiving nodes.
  Addressing –Each Ethernet header added in the frame contains the physical address (MAC address) that enables a frame to be delivered to a destination node.
  Error detection–Each Ethernet frame contains a trailer with a cyclic redundancy check (CRC) of the frame contents.
  Note: See sample CRC calculation @ https://asecuritysite.com/comms/crc_div

## Slide 31: Ethernet: Switch MAC Address Table
Before: PC1 broadcasts a frame.
After: PC3 replies to PC1.
Port 3: MAC PC3

## Slide 32: Hands-On #2: Ethernet Switch

## Slide 33: Network Protocols

## Slide 34: Network Protocols
Services of Network Protocols:
  Addressing end devices
  Encapsulation
  Routing
  De-encapsulating
Common network layer protocols include:
  IP version 4 (IPv4)
  IP version 6 (IPv6)

## Slide 35: IPv4

## Slide 36: IPv4: Classful

## Slide 37: IPv4: Private Addresses
Hosts that do not require access to the Internet can use private addresses
  10.0.0.0 to 10.255.255.255 (10.0.0.0/8)
  172.16.0.0 to 172.31.255.255 (172.16.0.0/12)
  192.168.0.0 to 192.168.255.255 (192.168.0.0/16)

## Slide 38: IPv4: Special Addresses
Network and Broadcast addresses–within each network the first and last addresses cannot be assigned to hosts
Loopback address–127.0.0.1 a special address that hosts use to direct traffic to themselves (addresses 127.0.0.0 to 127.255.255.255 are reserved)
Link-Local address–169.254.0.0 to 169.254.255.255 (169.254.0.0/16) addresses can be automatically assigned to the local host
TEST-NET addresses–192.0.2.0 to 192.0.2.255 (192.0.2.0/24) set aside for teaching and learning purposes, used in documentation and network examples
Experimental addresses–240.0.0.0 to 255.255.255.254 are listed as reserved

## Slide 39: IPv4: Limitation
IP Address depletion
Internet routing table expansion
Lack of end-to-end connectivity

## Slide 40: IPv6
128 bits in length and written as a string of hexadecimal values.
In IPv6, 4 bits represents a single hexadecimal digit, 32 hexadecimal value = IPv6 address:
  2001:0DB8:0000:1111:0000:0000:0000:0200
  FE80:0000:0000:0000:0123:4567:89AB:CDEF
Hextet used to refer to a segment of 16 bits or four hexadecimals.
Can be written in either lowercase or uppercase.

## Slide 41: IPv4 and IPv6 Coexistence

## Slide 42: Hands-On #3: OSPF Routing Protocol

## Slide 43: Application Protocols

## Slide 44: Application Protocols: Sample
Domain Name Service Protocol (DNS) – used to resolve Internet names to IP addresses.
Telnet – a terminal emulation protocol used to provide remote access to servers and networking devices.
Bootstrap Protocol (BOOTP) – a precursor to the DHCP protocol, a network protocol used to obtain IP address information during bootup.
Dynamic Host Control Protocol (DHCP) – used to assign an IP address, subnet mask, default gateway and DNS server to a host.
Hypertext Transfer Protocol (HTTP) – used to transfer files that make up the Web pages of the World Wide Web.

## Slide 45: Application Protocols: Sample
File Transfer Protocol (FTP) – used for interactive file transfer between systems.
Trivial File Transfer Protocol (TFTP) – used for connectionless active file transfer.
Simple Mail Transfer Protocol (SMTP) – used for the transfer of mail messages and attachments.
Post Office Protocol (POP) – used by email clients to retrieve email from a remote server.
Internet Message Access Protocol (IMAP) – another protocol for email retrieval.

## Slide 46: Hands-On #4: DHCP